## Slide 1
I²C Temperature Sensor
FPGA Implementation on Nexys A7 · Verilog RTL Design
Protocol
I²C (400kHz)
Sensor
TMP102 / Digilent
FPGA
Nexys A7-100T
Language
Verilog HDL
Communication Systems Laboratory

## Slide 2
System Architecture
Four hardware modules cooperate across two clock domains to acquire and display temperature data
TMP102
Sensor
i2c_master.v
FSM: 28 states SCL: 10 kHz SDA: bidirectional Addr: 0x97 (read)
clkgen_200kHz.v
100MHz ÷ 500 = 200kHz
seg7.v
BCD decode + multiplex
Nexys A7 FPGA
● 7-Seg Display (XX°C) ● 8 LEDs (binary temp) ● CLK: 100 MHz ● Reset: BTN-C
SDA/SCL
200kHz
temp[7:0]
8-bit temp
100 MHz Domain
Clock div → 200kHz → ÷10 → 10kHz SCL

## Slide 3
I²C Protocol — Core Concepts
Two-wire serial bus · Open-drain topology · Master-slave architecture · ACK/NACK handshake
SCL
SDA
START
7-bit Address (0x4B)
R/W
ACK↓
8-bit MSB Data
Open-Drain Bus
Both SDA and SCL are open-drain — devices can only pull low. A pull-up resistor holds the line HIGH when idle. This enables wired-AND logic and safe multi-master contention.
START / STOP Conditions
START = SDA falls while SCL is HIGH. STOP = SDA rises while SCL is HIGH. These are the only SDA transitions allowed on a HIGH clock — unique bus framing markers.
Address + ACK Frame
Master transmits 7-bit slave address + R/W̄ bit (8 total). Addressed slave pulls SDA LOW in the 9th clock cycle — the ACK. NACK (SDA stays HIGH) means no response.
Clock Stretching
A slow slave can hold SCL LOW to pause the master. The master must detect SCL held low and wait before proceeding. Not implemented here — sensor responds within one SCL period.

## Slide 4
I²C Master — Finite State Machine
28 states synchronized to 200 kHz clock · counter-gated transitions · bidirectional SDA control
POWER_UP
Wait 2000 clocks for sensor rail to stabilize
START
Assert SDA↓ while SCL HIGH; wait ¼ period
SEND_ADDR[6:0]
Shift out 7 bits of address 0x4B MSB-first
SEND_RW
Send R/W̄ = 1 (read operation)
REC_ACK
Release SDA; check slave pulls it LOW
REC_MSB[7:0]
Sample 8 bits of temperature MSB byte
SEND_ACK
Master drives SDA LOW → ACK to sensor
REC_LSB[7:0]
Sample 8 bits of temperature LSB byte
NACK + Restart
Master sends NACK; latch data; restart loop
↺ Continuous
polling
⏱ Timing Logic: Counter ticks at 200 kHz (5 µs/tick). Each state transitions on a specific count value separated by 20 ticks = exactly one 10 kHz SCL period. SDA is driven ¼ cycle after SCL edge to meet I²C setup/hold time.

## Slide 5
Clock Hierarchy & Frequency Division
100 MHz
Nexys A7 Crystal Oscillator
Module: clkgen_200kHz.v
counter counts to 4999
toggle at rollover
÷ 500
200 kHz
Generated intermediate clock
Module: i2c_master.v
counter counts to 9
toggle at rollover
÷ 20
10 kHz
SCL — I²C bus clock
Module: Sensor interface
Drives TMP102 SCL pin
I²C standard compliant
100 MHz ÷ (2 × 250) = 200 kHz | 200 kHz ÷ (2 × 10) = 10 kHz SCL
Why 200 kHz intermediate? — SCL needs ¼-period SDA setup time. 200 kHz gives 5 µs ticks; 20 ticks = 10 kHz SCL period; 5 ticks = setup margin.

## Slide 6
SDA Bidirectionality & Data Extraction
The single SDA wire changes direction dynamically — controlled by the FSM state register
Tristate SDA Control Logic
assign SDA_dir = (state == POWER_UP ||
state == START ||
state == SEND_ADDR* ||
state == SEND_ACK ||
state == NACK) ? 1 : 0;
assign SDA = SDA_dir ? o_bit : 1'bz;
assign i_bit = SDA; // always monitor
SDA_dir = 1 → MASTER transmits
FSM asserts o_bit onto wire. Slave sees data.
SDA_dir = 0 → MASTER receives
SDA driven to high-Z (1'bz). Slave can pull LOW. i_bit samples the line.
Wired-AND resolution
If master outputs 'z' and slave pulls LOW, SDA = LOW. This is how ACK is physically received.
Temperature Data Assembly
TMP102 returns 12-bit two's-complement temperature in 16 bits (MSB byte + LSB byte).
temp_data_reg <= { tMSB[6:0], tLSB[7] }; // 8-bit resolution: bits [14:7] of raw word = integer °C
tMSB[7] is the sign bit (discarded for positive temps). tLSB[7] is the 0.5°C fractional bit — included for rounding, then displayed as integer.

## Slide 7
7-Segment Display Controller
Multiplexed persistence-of-vision · BCD decode in hardware · 4 ms refresh cycle
Digit Assignment (anode_select)
AN=2'b00
C (Celsius symbol)
seg=100_0110
AN=2'b01
° (degree symbol)
seg=001_1100
AN=2'b10
ones digit (temp%10)
seg=lookup table
AN=2'b11
tens digit (temp/10)
seg=lookup table
Multiplexing Timing Logic
// 1ms per digit (4ms total refresh)
if(anode_timer == 99_999) begin
anode_timer <= 0;
anode_select <= anode_select + 1;
end
// 100 MHz × 10ns = 1 tick
// 100,000 ticks = 1 ms per digit
// 4 digits × 1ms = 4ms = 250 Hz
Hardware Division (No Division Unit!)
tens = temp_data / 10 → Verilog synthesizes this as a combinatorial divider (shift-subtract). No dedicated divide block — the synthesizer infers a ripple-borrow circuit from the / operator on 8-bit wires.
Segment encoding: 7-bit active-LOW — bit[6]=a, bit[5]=b … bit[0]=g. '0' lights a segment, '1' turns it off. Pattern 100_0000 = digit 0 (all except segment g).

## Slide 8
Results & Key Takeaways
✓ I²C Fully Implemented
Start, address frame, ACK, 16-bit read, NACK, restart cycle — all in hardware FSM.
✓ Real-Time Display
4 ms refresh via multiplexed 7-segment. Reads update continuously — no buffering lag.
✓ FPGA Demonstrated
Bitstream loaded on Nexys A7. Room temperature correctly shown on display and LEDs.
Communication Engineering Insights
→ Open-drain bus topology inherently prevents bus contention — any device can assert low without shorting a driven-high line.
→ SDA setup/hold relative to SCL is the core timing constraint — the 200 kHz intermediate clock provides deterministic 5 µs ticks for precise ¼-period margins.
→ ACK/NACK is a wired-AND pull-down — slave participation is passive; the master simply observes whether its own HIGH is overridden.
→ State machine counter-gating is a reliable synchronization strategy when two sub-clocks must maintain a phase relationship.